## Slide 1
VISION-ASSISTED CARTESIAN ROBOTIC SYSTEM FOR 3D BLOCK CONSTRUCTION
Ahmed Gharib
Mohie Halawa
Khalil Qanabita

## Slide 2
TABLE OF CONTENTS
Motivation & Objectives
Vision & Control System
Testing & Results
Conclusion & Future Work
Bill of Materials
System Design

## Slide 3
BACKGROUND & MOTIVATION
Why This Project?
• Industrial pick-and-place systems must do more than move parts.
• Real assembly cells must verify feeding, gripping, placement, and failures.
• Timing-based systems assume success instead of confirming it.
• The goal is a machine that verifies every stage rather than relying on assumptions.

## Slide 4
THE PROBLEM
WHAT AN OPEN-LOOP MACHINE CANNOT SEE
Stacking is sequential: block 7 has to be right or block 18 falls off it. A timing-based machine cannot tell success from failure, so it never stops — it turns one silent failure into a pile.
1
Empty or jammed hopper
The gate opens, no block comes out, the belt runs anyway. The claw closes on nothing.
2
Two blocks instead of one
A gate open far enough for one block is open far enough for two. The second arrives out of sequence.
3
A block that is late or crooked
A belt is not a positioning system. The block is picked by its corner, or missed entirely.
4
Lost steps
Open-loop steppers lose steps against a stall, and nothing in the motor reports it.
5
A hand in the workspace, or a controller reset
A person moves a block, or a USB open reboots the board un-homed. The machine's model is silently wrong.

## Slide 5
1
Develop a complete self-feeding robotic cell capable of autonomous 3D block construction.
OBJECTIVES
2
Place blocks at any addressable grid cell and stack level within the machine workspace.
3
Support both vertical and horizontal block orientations through a rotating end-effector and dual-grid system.
4
Detect, localize, and verify blocks using an overhead vision system with calibrated grid mapping.
5
Provide a browser-based platform for structure design, execution, and safe operation of the robotic system.

## Slide 6
SCOPE AND BOUNDARIES
WHAT “CLOSED-LOOP” MEANS IN THIS PROJECT
Sensor- and vision-confirmed sequencing — not servo position control.
The machine never verifies a motor shaft. It verifies that a block left the hopper, that a block reached the pickup point, that a build phase began and ended, and that a block is visible where one was commanded. Each of those can refuse permission for the step after it.
IN SCOPE
  CoreXY gantry, Z axis, servo claw, 90° rotation
  Self-feeding module with two ultrasonic confirmations
  Overhead fisheye camera, detection and grid calibration
  Browser console, 3D Build Studio, digital twin
  Two serial protocols and the Pi orchestration
OUT OF SCOPE
  Autonomous planning — the human designs the structure
  Interrupting a motion already in progress
  Metrological (checkerboard) camera calibration
  Closed-loop motor control — there are no encoders
  Multi-operator accounts and WebRTC video

## Slide 7
01
SYSTEM DESIGN
The three-controller architecture, the mechanics, and the components the machine is actually made of.

## Slide 8
Computer vision detects blocks and guides the robot to build predefined structures.
OVERALL SYSTEM ARCHITECTURE

## Slide 9
THREE CONTROLLERS, ONE MASTER
ONE MASTER, TWO ISOLATED SLAVES
Raspberry Pi 5
8 GB · THE MASTER
  Camera capture and the whole vision pipeline
  FastAPI web service, WebSocket event stream
  The Studio and the browser application
  Two-board orchestration
  Every safety gate and the session lock
Arduino MEGA 2560
THE GANTRY · 9600 8N1
  X, Y and Z step generation and direction
  Homing, hardware and software limits
  Grid-to-steps arithmetic, both grids
  Gripper servo and rotation stepper
  The fourteen-phase build cycle
Arduino Uno
THE FEEDER · 9600 8N1
  Two-stage hopper gate servo
  Conveyor belt stepper (A4988)
  Alignment servo
  Both HC-SR04 ultrasonic sensors
  The complete feed state machine
The two Arduinos have no wire between them and neither can command the other. That isolation is a safety property: permission to pick a block up can only be granted where the master can see it.

## Slide 10
HOW ONE BLOCK GETS BUILT
DESIGN › COMPILE › FEED › PLACE › VERIFY
1
DESIGN
A person places blocks in the Studio, on the machine's real lattice.
2
COMPILE
Sorted bottom-up, grouped by orientation, emitted as B col row level.
3
FEED
One block doubly confirmed out of the hopper and onto the pickup point.
4
PLACE
Only then the fourteen-phase pick, rotate, place and park cycle.
5
VERIFY
The camera watches; the twin mirrors the build from phase telemetry.
Nothing in this chain is advanced by a timer. Each stage waits for a durable terminal result from the stage before it, and a stage that cannot prove what happened stops the build instead of continuing.

## Slide 11
MECHANICAL DESIGN
    X-axis motion system
    Y-axis gantry
    Z-axis actuator
    End-effector (gripper)

## Slide 12
THE X/Y STAGE: COREXY
BOTH MOTORS OFF THE MOVING BEAM
Verified on the machine by watching the shafts
CoreXY skeleton and limit-switch homing after Greg06, “Automated Chessboard”, Instructables 2022. Z, the claw, the feeder, the camera and all three controllers were built on top of it.
  Same sense › the carriage walks along X. Opposed senses › it walks along Y.
  Two NEMA17 motors are fixed to the frame and drive one continuous GT2 belt path, so the beam stays light and the envelope stays large.
  Guidance is eight castor wheels on 3D-printed carriages running on the aluminium profile.
22.8 cm
X holder travel · 4,550 steps
38.0 cm
Y holder travel · 7,600 steps
200
steps per cm (X 199.6, Y 200.0)
4
limit switches, all NC
Homing drives each axis into its own switch; the corner where both are pressed is machine position (0, 0).

## Slide 13
Z AXIS AND END EFFECTOR
LIFT, GRIP, AND A QUARTER TURN
3D-printed two-jaw claw — the reference design's electromagnet is no solution for wooden blocks
Z axis
One NEMA17 on the moving carriage, on the 15 mm linear rail. 26.5 cm of travel, 1,350 steps.
Both ends are switches
Every build re-zeroes Z on the bottom switch and carries at the top. Neither end is a remembered number.
The claw
One servo, two positions: OPEN 0°, CLOSE 52°, on the block's 2.2 cm face. No sensor at all — hence a fixed 600 ms settle.
Rotation
A 28BYJ-48 through a ULN2003 turns the claw 512 of 2,048 steps at 10 rpm — the second block orientation.
The grip centre sits (−0.3, +0.6) cm off the rotation axis, so a 90° turn swings the block round that axis. That swing is corrected as a per-rotation tool offset — not as a grid error.

## Slide 14
THE FEEDER
DOSE EXACTLY ONE BLOCK — AND PROVE IT TWICE
1
Close
container shut
2
Open in two stages
20° › 90° › 160°
3
Wait for EXIT
a block left the hopper · 10 s
4
Shut the gate
before the belt starts
5
Run the belt
150 steps/s
6
Wait for STAGE
a block arrived · 15 s
7
Align
servo 90° › 120°
8
Re-read STAGE
it is still there
Two ends of the feed path, three measurements — and nothing after them is assumed.
Refuses to double-load
A feed request arriving while the stage sensor already sees a block is refused with stage_occupied — before anything opens.
A gate becomes a doser
The container shuts the instant EXIT fires, before the belt starts, so a second block cannot follow the first out.
Never a success it cannot see
If the block has gone after the aligner moves, the belt resumes instead of the feeder reporting staged.

## Slide 15
TWO GRIDS, NOT ONE GRID WITH A FLAG
ONE ENVELOPE, TWO LATTICES, ONE FEEDER CELL
VERTICAL · 2.2 × 6.0 cm
7 × 6 addressable, 41 buildable
pitch 3.8 × 7.6 cm
HORIZONTAL · 6.0 × 2.2 cm
3 × 10 addressable, 29 buildable
pitch 7.6 × 3.8 cm
cell [0,0] — the feeder, never built on; its centre is the home corner
One envelope
Both lattices share the same 22.8 × 38.0 cm holder travel — a block lying down does not move a limit switch.
One feeder cell
[0,0] is the feeder in both modes and is never built on: 7×6−1 = 41 standing, 3×10−1 = 29 lying.
+1.9 cm registration
(6.0 − 2.2)/2 = 1.9 — exactly the overhang of the rotated face, so horizontal [0,0] seats flush against vertical [0,0].

## Slide 16
Bill Of Material - 1 of 3
Components - Computing
Arduino MEGA
Raspberry Pi 5
Raspberry Pi 5 Camera Module

## Slide 17
Bill Of Material - 2 of 3
Components - Electrical and Power
3x NEMA17 Stepper Motor
3x TB6600 Driver
ULN2003 Driver
Stepper Motor 28BYJ-48
1X Servo Motor
4x Limit Switch
Adjustable Buck Converter
Power Supply, 12V 15A

## Slide 18
Bill Of Material - 3 of 3
Components - Mechanical
Linear Rail + Linear Motion Bearing
GT2 Belt
Timing Pulley
Bearing Wheels
Aluminum Profile

## Slide 19
POWER ARCHITECTURE
ONE 12 V RAIL, ONE 5 V RAIL, ONE COMMON GROUND
  12 V rail — the three TB6600 drivers and the A4988 on the feeder belt.
  5 V rail — an LM2596 buck converter feeds three servos, the ULN2003, both HC-SR04s and the A4988 logic.
  Both Arduinos — powered over USB from the Pi, which is also how they communicate.
Why 15 A is not overspecified
The build cycle moves one thing at a time, so the instantaneous draw is usually a single stepper plus logic.

## Slide 20
WIRING
TAKEN DIRECTLY FROM THE TWO FIRMWARE SOURCES
Arduino MEGA 2560 — three TB6600 drivers, four limit switches, gripper servo, ULN2003 rotation stepper
Motor and sensor runs use connectors rather than direct solder joints, so a motor can be swapped and the gantry dismantled for transport. There is no enclosure and no cable chain.

## Slide 21
02
VISION & CONTROL SYSTEM
What the camera sees, how a pixel becomes a cell, and the protocol that decides when the machine is allowed to move.

## Slide 22
ONE LENS, TWO COSTS
WHAT A 160° FISHEYE AT 50 CM BUYS, AND COSTS
A raw frame straight off the camera, before any correction
Sensor
OV5647, 5 MP, DORHEA module on the Pi 5 CSI bus
Lens
160° fisheye, mounted rigidly ≈ 50 cm above the surface
Capture
1296 × 972 through Picamera2 — the binned full-field mode
Why binned
It keeps the whole 23 × 38 cm workspace in one frame, and the per-frame cost inside budget
Lens model
Equidistant, 120° output — tuned by eye, not checkerboard-calibrated
THE TWO COSTS
  Severe barrel distortion — the aluminium rails are straight on the machine and curved in the image
  A colour cast strong enough to be a functional fault, not a cosmetic one

## Slide 23
THE VISION PIPELINE
ONE PROCESS OWNS THE CAMERA; ONE FIXED ROUTE
Colour correction runs once, at the captured frame
Applied immediately after orientation and before every detector, so every tool in the system sees identical pixels. Colour is deliberately not part of the saved projection identity.
Detection runs on a background worker
At a lower rate than the video, with the main loop drawing the last completed result. A slow analysis can never stall the stream.
The Pi picks the cell; the firmware turns it into steps
The saved homography converts a pixel to physical centimetres and then to a [col, row]. The Pi never needs a motor step to draw or select one.

## Slide 24
BLOCK DETECTION
A HYPOTHESIS, THEN AN ANSWER — THREE LAYERS
Ten blocks deliberately off the lattice — all ten found, everything else rejected
1
Segmentation
Warm material by red-minus-blue and red-minus-green, never by brightness — the work surface is overexposed, so a brightness cutoff selects the table and not the blocks.
2
Live overlay
Rejects, then rectifies: duplicates by IoU, boxes running off the frame (the rails), anything further than 0.34 cells from a lattice site (the holder offcuts).
3
Calibration
Runs once, deliberately, and is the only layer allowed to write a calibration.
TWO RULES KEEP THE OVERLAY HONEST — BOTH ASSERTED BY TESTS
  The measured centre is never snapped to the lattice — snapping would hide the misplaced block the overlay exists to show.
  The lattice filter never fires on a partial view: under six detections, or if it would reject over 30 % of what it saw, everything is kept.

## Slide 25
GRID CALIBRATION
WHERE THE MACHINE'S GRID SITS ON THE CAMERA IMAGE
One fiducial of the printed A2 calibration target
FOUR ROUTES, ONE ARTEFACT
  Four clicked corners — the fast fallback.
  Printed A2 colour target — the primary route.
  Evidence-assisted — pools frames when the gantry hides part of the sheet.
  Placed-block self-calibration — the rig places its own blocks, so the thing measured is the thing being calibrated.
HARD ACCEPTANCE GATES, NOT STATUS READOUTS
Colour parity
every fiducial the right way round
Measured aspect ratio
against the declared geometry
Mean and maximum residual
both must pass, not just be reported
≥ 95 % physical coverage
every row and column supported
Numerical conditioning
gate at 1e−5, inside a 30-order gap
A refusal still draws what it found — green for blobs that joined a lattice, red for those that did not.

## Slide 26
CONTROL HIERARCHY
THE PI DECIDES WHETHER; EACH ARDUINO DECIDES HOW
HIGH LEVEL · RASPBERRY PI
  Chooses the target cell, the stack level and the grid mode
  Sequences the feeder before the gantry
  Applies every safety gate and owns the session lock
  Decides whether a command may be issued at all
  Never sends a motor step, a direction bit or a delay
LOW LEVEL · MEGA AND UNO
  Step generation, direction polarity, homing, limits
  The grid-to-steps arithmetic for both modes
  Servo and stepper timing, the phase sequence
  The feed state machine, belt rate, sensor thresholds
  Everything that cannot change without reflashing
WHY THE BOUNDARY IS DRAWN THERE
The firmware owns the step caps, the Z calibration, the servo angles, the pin map and the direction polarity — physical facts nothing can push over serial, so a stale copy on the Pi would be a lie nobody notices until the rig drives into something. A handful of values genuinely exist twice, and an automated test parses the live sketch and fails if either side has moved.

## Slide 27
THE ACKNOWLEDGEMENT PROTOCOL
ONE LINE FOR THE HUMAN, ONE LINE FOR THE PI
BUILD COMPLETE - block placed at [3,5] level 0
Place time: 31.6s
@12 OK col=3 row=5 level=0
Every machine line starts with @ — a character no other line in either sketch begins with, so the Pi's filter is one string test. Key=value and not JSON because on an 8 KB AVR at 9600 baud braces and quotes cost SRAM and airtime for nothing.
EIGHT KINDS · FOUR OF THEM TERMINAL
BOOT
READY
RECV
STEP
ERR
SAFE
HELD
OK
Filled = terminal. Exactly one terminal acknowledgement per command.
SAFE
Refused on validation. Nothing moved, and a retry is fine.
HELD
Failed part way through. The claw may still be gripping a block and the position is unknown. It needs a person.
They are separate kinds rather than a flag, so that Pi-side code cannot collapse them into a generic “if not ok: retry”. The retry is the thing that breaks the machine.

## Slide 28
THE FOURTEEN-PHASE BUILD CYCLE
EVERY PHASE ANNOUNCED BEFORE IT RUNS
1
raise_clear
Raise Z into the top switch
2
home_feeder
Home X/Y to the feeder cell [0,0]
3
neutralise_claw
Return the claw to neutral
4
open_claw
Open the jaws, still clear above
5
lower_to_ground
Lower Z into the bottom switch — re-zeroes Z
6
grip
Close the claw. The block is held
7
lift_block
Raise Z to carry height
8
move_to_target
Home, then Y to the row, X to the column
9
rotate_to_grid
Apply the active grid's rotation
10
lower_to_level
Lower Z to the target level
11
release
Open the claw. The block is placed
12
park_clear
Raise Z clear of the block just placed
13
park_home
Return X and Y to the origin
14
park_rotation
Return the claw to neutral
Phases 1–11 place the block; 12–14 park the rig. Parking is not decoration — placed but not parked is not a success, and the terminal result is downgraded from OK to HELD.

## Slide 29
ONE MESSAGE AUTHORISES MOTION
THE TWO-BOARD HANDOFF, AND THE FIVE LAYERS ABOVE IT
THE HANDOFF
Pi › Uno
FEED <id>
Uno › Pi
@id RECV / ACK / STATE / SENSOR / EVENT
Uno › Pi
@id OK state=block_ready result=staged
Pi › MEGA
B <col> <row> <level>
MEGA › Pi
@seq STEP step=n/14 phase=… status=begin
MEGA › Pi
@seq OK col=… row=… level=…
Only that one terminal message, with a matching id, authorises the B.
  ACK, STATE, SENSOR and EVENT are progress, never success. A terminal with the wrong id is ignored.
  After the B is sent, even a SAFE rejection locks the session — a block is already staged.
THE GUARD STACK
1
HTTP route
unconfirmed request · mismatched command · stale frame · locked session
2
Build worker
a second build already running
3
Safety state
a locked session, or no cell selected
4
Two-board handoff
another placement already owns the pickup point
5
Serial clients
an overlapping transaction, or the wrong board
The browser is a mirror — a greyed-out button is never the safety mechanism.

## Slide 30
THE OPERATOR CONSOLE
LIVE CAMERA, TAP A CELL, TWO TAPS TO MOVE
Tap a cell.
Selection moves nothing and shows the exact command, B 3 2 1.
Tap BUILD, then CONFIRM.
One correlated FEED, then the B. Two deliberate taps.
Three outcomes.
PLACED (green, selection cleared), REJECTED (amber, nothing moved), ABORTED (red, session locked).
No cancel, no retry.
There is no such control, because the machine cannot honour either.

## Slide 31
THE 3D BUILD STUDIO
DESIGN, VALIDATE, COMPILE — THEN RUN IT
THE VALIDATOR ASKS THREE QUESTIONS
  Support — a centre-of-mass toppling test, not a contact-ratio shortcut.
  Collision — in machine space, not grid indices, so a horizontal block spanning two columns is checked correctly.
  Reachability — inside the active grid, under the firmware's build ceiling.
THE COMPILER RUNS IN FOUR STEPS
  Support graph — which blocks rest on which, from footprint overlap.
  Ordering — Kahn's algorithm, bottom-up, grouping same-orientation runs to minimise mode latches.
  Emission — a mode command only on an actual change.
  Summary — blocks, latches, levels and a time estimate.
Deterministic — twenty compiles, byte-identical output. An invalid model compiles to nothing at all, never to a half-program.

## Slide 32
THE LIVE DIGITAL TWIN
IT DRAWS WHAT THE FIRMWARE SAID — AND NOTHING ELSE
It never invents state.
A block is drawn as placed because the server reported a terminal placed result for it, and for no other reason.
After an abort it stops.
A locked session freezes the animation, desaturates every block and demotes everything unconfirmed to a ghost.
Phase-driven, not clock-driven.
An earlier version interpolated a 1.6 s descent from the browser's clock and looped it — a 40 s build showed twenty-five descents that never happened.
If Z jams,
the block glides down, stops just short of the cell and sits there visibly not landing — which is the truth.

## Slide 33
03
TESTING & RESULTS
Sixteen complete builds on hardware, two reference boards, and 560 automated tests.

## Slide 34
TESTING METHODOLOGY
EVERY QUESTION ANSWERED AT THE CHEAPEST HONEST LEVEL
1
Automated software tests
no hardware
Grid arithmetic, protocol parsers, the compiler, the twin, the homography. The Python and TypeScript grids are held to each other by shared fixtures.
2
Protocol-level simulation
no hardware
A fake MEGA and a fake Uno speak the same acknowledgement grammar, including failure, reset and cancellation. This is how the two-board handoff was tested exhaustively.
3
Firmware host builds
no hardware
A stub-Arduino harness proves the sketch parses and that its output is byte-for-byte the protocol. A clean compile is not treated as a test of behaviour.
4
Hardware runs on the rig
the real machine
Anything touching motion, limits or Z. Every run appends to two logs — a stopwatch per build, and every serial line with the gap since the last one.
The rig takes half a minute to answer one question, and a wrong answer can drive a claw into a stack — so the logs from level 4 are the primary evidence, and everything else is rehearsal.

## Slide 35
CYCLE TIME AND REPEATABILITY
SIXTEEN BUILDS ON HARDWARE, ALL SIXTEEN PLACED
26.1 s
mean cycle, per block
19.8 – 32.2 s
fastest and worst case
< 45 s
the objective
12.57 s
the nine fixed phases
0.18 s
their standard deviation
Mean duration of each build phase, over sixteen builds (seconds)
Light bar = minimum to maximum across all sixteen · solid bar = mean
1
0.42
2
0.58
3
0.41
4
0.93
5
2.91
6
0.95
7
2.89
8
4.53
9
0.49
10
2.80
11
0.71
12
2.76
13
4.68
14
0.52
build phase 1 – 14
Nine phases never move
Nine of the fourteen have no distance or level dependence at all. Across all sixteen builds they summed to 12.57 s ± 0.18 s — six of them identical to the 0.01 s logging resolution.
The variation is travel, and nothing else
Only phases 8 and 13 range widely, 1.48 s to 8.53 s. With no acceleration ramp, a move of N steps takes N times a fixed period.

## Slide 36
VISION RESULTS
TWO REFERENCE BOARDS, TWO NEGATIVE RESULTS
29 / 29
blocks found, both boards
33 › 29
hypotheses after rejection
37 – 103 ms
per analysed frame
0.85 px
mean fit residual
0.27 cm
mapping error on a 2.2 cm block
29 blocks, the rails, and two wooden offcuts that are not blocks
WHAT THE FIT CHOSE, AND WHY
  Chosen on held-out prediction, not training error. Similarity 101.4 px, affine 1.38, homography 1.22, homography + curvature 1.09.
  Pitch is static to within 2 %. X 29.38 px (sd 1.24), Y 69.14 px (sd 1.08).
  An independent geometry check. The view is 17.7 % anisotropic; two independent estimates agree to 4 %.
The 0.27 cm is the saved four-corner format flattening the fit — not the fit itself.
TWO NEGATIVE RESULTS
Higher resolution finds nothing extra
29/29 at every width from 384 to 1024 px. Illumination flattening costs up to 3,894 ms a frame and finds exactly the same 29.
White balance is right for the sheet, wrong for the board
On the printed sheet it takes the green mask from 0 pixels to 87,836. On a board of blocks it pulls the wood toward the surface: 28 of 29 with it on, 29 with it off.

## Slide 37
04
CONCLUSION & FUTURE WORK
What the machine proves, the limits that are real, and the one item on the list that is not optional.

## Slide 38
LIMITATIONS, STATED PLAINLY
LIMITS OF THE HARDWARE, NOT OF THE APPROACH
No hardwired emergency stop
Nothing removes motion energy independently of the software. The stop of last resort is the supply. The machine is run attended.
Motion cannot be interrupted
The gantry does not read serial while it moves, so software stop is stop-after-current-block by construction.
No watchdog
If the Pi crashes or the cable is pulled, the MEGA finishes the command it already holds.
Open-loop steppers, no stall detection
No encoders, no current sensing. A stall produces step pulses that go nowhere.
The lens is tuned, not calibrated
Adjusted by eye against straight edges — visually straight, not measurement-grade. The file records source: estimated.
The claw angle is not sensed
The operator is trusted to start neutral. If not, every placement that session is turned 90°.
And the layer that would let the camera notice a block that never arrived — placement supervision — is fully designed and not built.

## Slide 39
FUTURE WORK
ONE ITEM IS NOT OPTIONAL; THE REST ARE
SAFETY, FIRST
  A hardwired emergency stop — a latching mushroom button in series with a contactor on the 12 V motor rail
  A stop that is observable during motion, and a communications watchdog that brings the rig to a defined state
Close the loop on placement
  A server-side ledger of what went where
  Compare at the park state — a known, repeatable position
  A pick-from-cell verb, so the machine can act on a wrong placement
Measure properly
  A checkerboard or ChArUco lens calibration
  A per-cell table in the saved map, removing the 0.27 cm flattening error
  Fix the camera, not the matrix — the colour correction is at its limit
Protocol and capability
  Controller-supplied command ids
  Encoders or stall detection — also worth about a third of the cycle time
  A faster serial link, and a larger workspace

## Slide 40
CONCLUSION
THE CONTRIBUTION IS NOT THE GANTRY
Cartesian gantries are a solved problem. What this project demonstrates is the layer student-scale automation usually leaves out: every physical transition confirmed by something other than a clock.
The feeder
reports success because a sensor saw a block — and saw it again after the aligner moved.
The gantry
narrates each of its fourteen phases before running it.
The twin
draws what the firmware said, and stops short of the cell until the release event arrives.
And when it cannot prove
what happened, it locks and asks for a person rather than retrying.
16 / 16
hardware builds placed
26.1 s
mean cycle
5
levels on one cell
29 / 29
blocks detected
560
automated tests

## Slide 41
THANK YOU
QUESTIONS
Ahmed Gharib · Mohie Halawa · Khalil Qanabita
Supervised by Dr. Samer Arandi
Department of Computer Engineering · An-Najah National University